Mark Nandor

Problem Set 8

Part 1 – Camera Calibration angle

The camera is set at an offset yaw angle to the global coordinate frame. In order to determine what this angle is, the block is placed at world coordinates (0.5m, 0.5m), and (0.75m, 0.5) in Gazebo. The corresponding camera (u,v) pixel coordinates are (292.94, 182.9) and (376.29, 166.28), respectively. The camera offset yaw angle is the angle between the resultant unit vectors in world and camera space. Calculating the arctangent yields a camera rotation angle of -0.196 radians. Thus, all camera coordinates should be rotated by the inverse (+0.196 radians) to make them aligned with the world coordinate frame.

Part 2 – Camera linear transformation

Once the camera yaw offset is calculated and applied, the block centroid pixels are in a coordinate frame aligned with the global frame. Observation showed that camera u corresponded linearly with world x, and camera v corresponded linearly with world y. Observations were made, and the following linear transformations were established:

Camera U vs. Block X
After Rotation
Camera X - Pixels
Block X - meters

Camera V vs. Block Y
After Rotation
Camera V - Pixels
Block Y - meters
Contained in these equations is the meter to pixel ratio (0.003 meters per pixel), as well as the camera offset of 0.2488 m in x and 1.2217 m in y. Applying these equations to the post rotation pixel measurements accurately translates them into world coordinates.

Part 3 – Block Orientation Finder

In the red pixel finding set of for loops, a dynamic matrix was established that contained all camera u,v red pixel pairs. For simplicity’s sake, all of the points were converted into world (x,y) coordinates. From there, the centroid position was subtracted off, and the covariance found of the resultant matrix. Eigenvalues and eigenvectors were computed of the covariance matrix, with the eigenvector of the largest eigenvalue corresponding to the major axis of the block. The arctangent of the vector was calculated, resulting in the orientation of the block in world space.

Notes: Eigen required a resize of the pixel matrix in every iteration. However, the function .resize() would alter some of the existing values in the matrix. The correct approach is call .conservativeResize(), which alters the matrix size while retaining current values.

The results are shown below: the block orientation according to Gazebo, and block orientation computed by the ROS node.